School of Computer Science

60-265-01 Computer Architecture and Digital Design

Winter 2010

Midterm Examination # 1

Wednesday, February 10, 2010

SAMPLE ANSWERS

Student Name: ________________    ___________________

First Name                 Family Name

Student ID Number: _____________________

Duration of examination: 75 minutes

- 1. Answer all questions on this examination paper in the space provided.

- 2. This is a closed-book examination – no notes or books or electronic computing or storage devices may be used.

- 3. Do not copy from other students or communicate in any way. All questions will be answered only by the attending proctors.

- 4. All students must remain seated during the last 5 minutes of the examination.

- 5. The examination must be surrendered immediately when the instructor announces the end of the test period.

- 6. Each student must sign the examination list before leaving the classroom.

Total mark obtained: ____________________

Maximum mark: 42

Question 1. [ 6 marks ]

Using Boolean algebra, prove the following theorems.  For each step in the proofs state the specific axiom that is used.  Each part is worth 3 marks.  [NOTE:  The full list of all axioms is provided for each student on the last page of this examination.]

- X+X = X

Proof:

X+X  	= (X+X)1			Identity

= (X+X)(X+X’)	     Complementation

= X+(XX’)	     	Distributivity

= X+0			Complementation

= X				Identity

- X’ + XY = X’ + Y

Proof:

Collapse Theorem (see lecture notes)

X’ + XY 	= (X’ + X).(X’ + Y)	Distributivity

= 1.(X’ + Y)		Complementation

= X’ + Y			Identity

Question 2. [ 13 marks ]

Answer each question below.

- Convert the decimal number -271 to a signed-binary number using a 16-bit representation of 2’s complement form of integer. [ 3 marks ]

Start by converting the absolute value:

271 / 2 = 135    rem  1   least significant (rightmost) bit

135 / 2 =  67    rem  1

67 / 2 =  33    rem  1

33 / 2 =  16    rem  1

16 / 2 =   8    rem  0

8 / 2 =   4    rem  0

4 / 2 =   2    rem  0

2 / 2 =   1    rem  0

1 / 2 =   0    rem  1   most significant (leftmost) bit

Gathering bits yields the 9-bit result:   100001111

Now convert to 16-bit signed binary form.  First add seven 0-bits (‘padding bits’) to the left side.

0000000100001111   Padded absolute value

1111111011110000   Complement

1111111011110001   Add 1 – Final answer

- Convert the octal number 4136758 to a hexadecimal number. [ 2 marks ]

Write octal digits as binary – groups of 3 bits per octal digit

= 100 001 011 110 111 101

Rearrange bits (from right) in groups of 4 bits and pad with zeros on the left, as required

= 0010 0001 0111 1011 1101

Convert each 4-bit group to a hex-digit

Answer:  = 217BD

- Convert the positive decimal real number 1.1 to an unsigned binary number. [ 2 marks ]

Separate the number 1.1 into its integer and fractional parts and convert each separately.  First, convert the integer:

1 / 2  =   0   rem  1			( 1

Next, convert the fraction:

0.1 x 2  = 0.2	integer  0

0.2 x 2  = 0.4	integer  0

0.4 x 2  = 0.8	integer  0

0.8 x 2  = 1.6	integer  1

0.6 x 2  = 1.2	integer  1

0.2 x 2  = 0.4	integer  0 Repeats the last 4 steps

Answer:	( 0.0[0011]

Where the bits within braces repeat.

- Convert the positive decimal real number 4.375 to an unsigned binary number. [ 2 marks ]

Separate the number 4.375 into its integer and fractional parts and convert each separately.  First, convert the integer:

4 / 2  =   2   rem  0

2 / 2  =   1   rem  0

1 / 2  =   0   rem  1			( 100

Next, convert the fraction:

0.375 x 2  = 0.75	integer  0

0.75  x 2  = 1.5	integer  1

0.5   x 2  = 1.0	integer  1

Stop here because fraction part is ZERO!

Answer:	( 0.011

Note that this value is just 3/8 which, of course, is 0.375 expressed as a rational number.

- State the exact values of the largest positive value and the smallest negative value that can be defined in an L-bit representation using signed-binary (ie. 2’s complement) notation. [ 2 marks ]

Largest positive value:     2L-1 - 1

Smallest negative value:	-2L-1

- State the exact number of different (ie. unique) bit arrangements that can be represented in an L-bit representation. [ 1 mark ]

Number of unique bit arrangements in L bits:  2L

- State the 16-bit BCD representation of the number 691810  in binary form (ie. as 16 bits). [ 1 mark ]

Answer:   691810  =  0110 1001 0001 1000

Question 3. [ 9 marks ]

Part A.  State the six (6) fundamental logic gates (excluding the inverter) and, for each gate, provide a complete truth table that fully defines the logic of each gate.  Each correctly identified gate and truth table is worth 1 mark.  [6 marks]

| AND |  |  |  | OR |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| X/Y | 0 | 1 |  | X/Y | 0 | 1 |
| 0 | 0 | 0 |  | 0 | 0 | 1 |
| 1 | 0 | 1 |  | 1 | 1 | 1 |

| NAND |  |  |  | NOR |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| X/Y | 0 | 1 |  | X/Y | 0 | 1 |
| 0 | 1 | 1 |  | 0 | 1 | 0 |
| 1 | 1 | 0 |  | 1 | 0 | 0 |

| XOR |  |  |  | XNOR |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| X/Y | 0 | 1 |  | X/Y | 0 | 1 |
| 0 | 0 | 1 |  | 0 | 1 | 0 |
| 1 | 1 | 0 |  | 1 | 0 | 1 |

Part B.  State the five (5) principal components of the von Neuman architecture for a stored program digital computer. [ 3 marks ]

RAM – volatile memory

CPU – central processing unit

Bus – interconnection network (connects all other components)

Mass storage – non-volatile storage

I/O – peripheral devices for user input/output

Question 4. [ 8 marks ]

Answer all parts of this question. In each part you may use only Boolean algebra and fundamental postulates – truth tables are not permitted.

Part A. Simplify the following Boolean expression using Boolean algebra (no truth tables or Karnaugh maps).  Express your answer in both SOP and POS forms. [3 marks]

A’BC + ABC’ + ABC

ANSWER:

A’BC + ABC’ + ABC	= (A’+A)BC + AB(C’+C)

= BC + AB

Final Answer:	= BC + AB (SOP), B(A+C) (POS)

Part B.  Simplify the following Boolean expression using Boolean algebra. [2 marks]

(BC’ + A’D)(AB’ + CD’)

ANSWER:

(BC’ + A’D)(AB’ + CD’)

= BC’AB’ + BC’CD’ + A’DAB’ + A’DCD’

(BC’AB’=ABB’C’=0, same way BC’CD’=0,... )

= 0 + 0 + 0 + 0

= 0    Final Answer

Part C.  Using De Morgan’s theorem and Boolean algebra, show that:  [3 marks]

(AB)’+(A’B’)’ = 1

ANSWER:

(AB)’+(A’B’)’

= (A’+B’)+(A’’+B’’) = A’+B’+A+B = 1+1 = 1

Question 5. [ 6 marks ]

Part A. [ 3 marks ]

Simplify the following Boolean SOP expression using the Karnaugh map technique.  Express your answer in SOP form.

F(X,Y,Z) = ∑ m(0,2,5,6)

ANSWER:

| Kmap | YZ/00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| X/0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 0 | 1 |

The resulting SOP form is:

F = X’Z’ + XY’Z + YZ’

Part B. [ 3 marks ]

Simplify the following Boolean SOP expression, with don’t care conditions, using the Karnaugh map technique.  Express your answer in SOP form.

F(W,X,Y,Z) = ∑ m(0,2,5,6,8,12)

dc(W,X,Y,Z) = ∑ m(1,4,10,15)

ANSWER:  (D is used for don’t care values)

| Kmap | YZ/00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| WX/00 | 1 | D | 0 | 1 |
| 01 | D | 1 | 0 | 1 |
| 11 | 1 | 0 | D | 0 |
| 10 | 1 | 0 | 0 | D |

NOTE:  Remember the D values can be chosen arbitrarily.

The resulting SOP form is:

F = Y’Z’ + W’Y’ + W’Z’

This page contains information provided freely for each student to use for the examination, if required.  You may detach this page.

Boolean Postulates:

P0:  Existence: There exist at least two elements x,y in B such

that x ≠ y

P1:  Closure: For every x,y in B there exist two combinational

operators + and . where (x+y) is in B and (x.y) is in B

P2:  Identity: There exist identity elements 0,1 in B relative to

the operations + and ., such that for every x in B:

0+x = x+0 = x and 1.x = x.1 = x.

P3:  Commutativity:  The operations + and . are commutative for

all x,y in B:

x+y = y+x and x.y = y.x

P4:  Distributivity: Each operation + and . is distributive over

the other; that is, for all x,y,z in B:

x.(y+z) = x.y+x.Z and x+(y.z) = (x+y).(x+z)

P5:  Complementation:  For every element x in B there exists an

element ~x, called the complement of x, satisfying:

x+~x = 1 and 	x.~x = 0